USE OF EMERGENCY RETRACTION HARNESS
FOR KWICKEE LEVEL BEST LEVELERS

If the control board is not working, the harness can be used to raise all jacks.

Remove the four screws holding the display/keyboard and pc board in the housing and remove entire assembly from the housing. Unplug the two connectors from the pc board.

Plug the large connector on the emergency harness into the large connector that was unplugged from the pc board.

Start the engine so maximum voltage will be available.

Plug the small connector on the emergency harness into the small connector that was unplugged from the pc board.

The hydraulic pump should start and the four solenoid valves should open causing all jacks to retract.

After jacks have been fully retracted, immediately disconnect the 4-way connector

on the jumper assembly from the wire harness to shut off the pump .

Failure to immediately remove the 4-way connector can cause over-heating

of the pump motor and permanent damage to the system.

Remove the large connector of the jumper assembly from the wire harness